## Slide 1: Options
Kevin

## Slide 2: Overview
User Interface
  Access custom functions
  Access flight controller functions
  Easily plan missions using a combination of custom and flight controller functions
Configuration Management/Continuous Integration
  Repeatable and reproducible build chain
  Track and maintain versions
  Easy interaction during testing/operation (using standard services, configuration, streaming, etc.)
  ICD configuration, access to flight controller, image streaming location, etc.
Mission Management
  Integrates custom modules
  Manages mission workflow between custom modules and flight controller functions
  ICD MAVlink overrides & extensions, waypoint types, UI hooks, etc.

## Slide 3: User Interface
Mission Planner
  Supports plugins - not well documented, only add menu options
  Could make custom UI and launch a “CAT UI” from within Mission Planner
  Lots of configuration options (motor test, esp8266, etc.)
  Supports APM
APM Planner 2.0
  No plugin framework
  Cross platform
  Supports APM
QGroundControl
  Supports plugins - decent documentation, add custom widgets via QML
  Cross Platform
  Supports PX4 and APM
Tower, UGCS, Custom, etc.

## Slide 4: Companion Computer CM/CI
Manual (Build Log)
  Time consuming
  Small differences, not as well documented
Maverick
  Well organized
  Poorly optimized
  Questionable maintenance practices
APSync
  Not actively developed
  Limited features
FlytOS
  Lots of proprietary modules
  Developer SDKs
Script-based
  Repeatable, reproducable, runnable in web-based tools
  Maintenance required
  Very customizable/portable

## Slide 5: Flight Controller Interface
MAVProxy
  Resource intensive
  Easy to use
MAVlink-router
  Basic features
  Very fast
MAVROS
  ROS environment opens up lots of possibilities
  Limited GCS connections
MAVProxy or MAVlink-router combined with MAVROS

## Slide 6: Firmware Comparison
PX4
Ardupilot

## Slide 7: Firmware Comparison
PX4
Better developer docs
Easy to use 3d simulation
BSD license
Better integration with MAVROS
Ardupilot
Better user docs
3d simulation limited
GPL license
Better integration with Dronekit
Both
Support more advanced navigation/stabilization (terrain following, optical flow, weathervane, VTOL, etc.)
Support similar range of lidar, sonar, rtk gps, airspeed sensors

## Slide 8: Way Ahead Strategy
Companion Computer CM/CI
  Continue developing scripts, goal is to get to a point where everyone can create an image from a web page with various options, then add features/supported CCs from there
  Document package versions and service definitions and keep them updated, come up with convention so we always know what is installed and how it’s configured
Mission Management
  For now, make sure our custom solutions use the same methods for reconfiguration, video streaming, etc. so we can more easily integrate later
Flight Controller Interface
  Document standard UDP ports for services, choose MAVProxy/MAVlink-router based on CC, use MAVROS in conjunction with a mavlink proxy
User Interface
  More research needs to be done, this will be influenced by Mission Management framework
Firmware
  Install PX4 on a quad and a plane and test

## Slide 9: Ingesting Solutions
There are many open source ROS solutions available and it is not much work to wrap code in a ROS node
Most of our Govt. solutions already use ROS nodes
In the future, a more formalized ICD would be beneficial, so that we can include custom commands and UI elements in planning autonomous missions
  ICD specifies topic for streaming video artifacts
  ICD specifies configuration scheme
  ICD specifies any new commands the custom nodes make available